## Slide 1: ECE 105: Introduction to Electrical Engineering
Lecture 12
Optoelectronics
Yasser Khan
Rehan Kapadia

## Slide 2
CMOS (Complementary MOS) Inverter

## Slide 3
CMOS (Complementary MOS) Inverter

## Slide 4
CMOS (Complementary MOS) Inverter

## Slide 5
CMOS (Complementary MOS) Inverter

## Slide 6: Qualitative discussion: n-MOSFET
VG > VT ; VDS  0
ID increases with VDS
VG > VT; VDS small, > 0
ID increases with VDS , but rate of increase decreases.
VG > VT; VDS  pinch-off
ID reaches a saturation value, ID,sat The VDS value is called VDS,sat
VG > VT; VDS > VDS,sat
ID does not increase further, saturation region.

## Slide 7: Quantitative ID-VDS Relationships – 1st attempt “Square Law”
;
ID will increase as VDS is increased, but when VG – VDS = VT, pinch-off occurs, and current saturates when VDS is increased further. This value of VDS is called VDS,sat. i.e., VDS,sat = VG – VT and the current when VDS= VDS,sat is called IDS,sat.
;
Here, Cox is the oxide capacitance per unit area, Cox = ox / xox

## Slide 8: ID-VDS characteristics for n-MOSFET
Saturation
region
Linear
region

## Slide 9: P-MOSFET N-MOSFET IV Characteristics
The PMOS IV is qualitatively similar to the NMOS IV, but the current is about half as large. Why?

## Slide 10: Threshold and Subthreshold

## Slide 11: Subthreshold Current
I
d
s
(
m
A
/
m
m
)
Vgs
The leakage current that flows at Vg<Vt is called the subthreshold current. Previously we had assumed that current is zero, but in reality that’s not the case.
90nm technology. Gate length: 45nm for NMOS, 50nm for PMOS
The current at Vgs=0 and Vds=Vdd is called Ioff.
Intel, T. Ghani et al., IEDM 2003

## Slide 12: The seven-segment display

## Slide 13: Light-based devices

## Slide 14: Artificially generating light

## Slide 15: LED emission spectra

## Slide 16: Direct vs indirect semiconductors
2 Energy band diagrams and major carrier transition processes in indium phosphide (direct bandgap) and silicon (indirect bandgap) crystals. Silicon, Germanium and some III/V compounds like GaP and AlAs are indirect bandgap semiconductors. InP, GaAs, GaN and other ternary (AlGaAs, InGaAs) and quaternary (InGaAsP, InAlAsP) compounds are direct bandgap semiconductors commonly used for photonic devices fabrication.

## Slide 17: LEDs are made out of non-silicon semiconductors

## Slide 18: LED symbols

## Slide 19: LED driver circuit

## Slide 20: LED driver circuit

## Slide 21: LED is a diode

## Slide 22: LED packages

## Slide 23: IV characteristics for LEDs

## Slide 24: Blue LED won the 2014 Nobel in Physics

## Slide 26: Steps to get the Blue LED
Notes: Experiments everyday for 1.5 years

## Slide 27: InGaN LEDs

## Slide 28: LED colors – single color from on LED

## Slide 29: Changing emission colors – can you change color?
Notes: GaN blue more in

## Slide 30: How to get white light

## Slide 31: The LED in our demo board
https://fscdn.rohm.com/en/products/databook/datasheet/opto/led/chip_mono/csl0416wbcw1-e.pdf
Notes: Blue peak and second peak from Yttrium Aluminum Garnet (YAG) LED Phosphor

## Slide 33: How does a photodiode work

## Slide 34: How does a photodiode work

## Slide 35: How does a photodiode work

## Slide 36: Photodiode

## Slide 37: IV of photodiode

## Slide 38: The PD in our demo board
https://www.vishay.com/docs/83493/vemd2023slx01.pdf

## Slide 39: PD characteristics

## Slide 40: LED-PD combo