## Slide 1: ECE 105: Introduction to Electrical Engineering
Lecture 2
System design and intro to Arduino
Yasser Khan
Rehan Kapadia

## Slide 2: Breaking down engineering systems
Any signal, for example temperature, touch, brain signal, video inputs, etc.
Temperature sensors, resistive touchscreen, brain electrodes, camera, etc.
Modules in ECE 105: circuits, devices
Processing circuits, analog and digital computing, etc.
Modules in ECE 105: biosensor, linear algebra, neural network, optical comm
Industry positions in apple, intel, meta, neuralink, etc
Industry positions in NVIDIA, Raytheon, Qualcomm, etc

## Slide 3: Breakdown of hardware and software
Hardware + Software
Hardware
Our own sensors + Arduino
Software running in Arduino + python (jupyter notebook)

## Slide 4: Equivalence to human body

## Slide 5: Oximeter system breakdown
Sensors
Processing
Information

## Slide 6: Resistive touchscreen system breakdown
Sensors
Processing
Information
Real world
S1
S2
S4
S5
S7
S8
S3
S6
S9

## Slide 7: Resistive touchscreen system approach
Goal
S1
S2
S4
S5
S7
S8
S3
S6
S9
Build a sensor that can detect touch
3.3V
GND
50 Ω
50 Ω
50 Ω
50 Ω
50 Ω
50 Ω
100 Ω
100 Ω
100 Ω
100 Ω
Connect to Arduino for processing
Get location from the voltage measurement

## Slide 8: Voltage
Voltage is the pressure from an electrical circuit's power source that pushes charged electrons (current) through a conducting loop, enabling them to do work such as illuminating a light. In brief, voltage = pressure, and it is measured in volts (V). The term recognizes Italian physicist Alessandro Volta (1745-1827), inventor of the voltaic pile—the forerunner of today's household battery. In electricity's early days, voltage was known as electromotive force (emf).

## Slide 9: Voltage

## Slide 10: Flow of charge – current
Current is the rate at which electrons flow past a point in a complete electrical circuit. At its most basic, current = flow.
An ampere (AM-pir), or amp, is the international unit used for measuring current. It expresses the quantity of electrons (sometimes called "electrical charge") flowing past a point in a circuit over a given time.
A current of 1 ampere means that 1 coulomb of electrons—that's 6.24 billion billion (6.24 x 1018) electrons—is moving past a single point in a circuit in 1 second.

## Slide 11: Increasing voltage / increasing water pressure

## Slide 12: Voltage difference

## Slide 13: Resistance
Resistance is a measure of the opposition to the flow of current in an electrical circuit. It is influenced by the material's properties, length, cross-sectional area, and temperature.

## Slide 14: Ohm’s law

## Slide 15: Ohm’s law

## Slide 16: Resistors
https://www.calculator.net/resistor-calculator.html

## Slide 17: Resistors

## Slide 18: Going back to the touchscreen
Build a sensor that can detect touch
3.3V
GND
50 Ω
50 Ω
50 Ω
50 Ω
50 Ω
50 Ω
100 Ω
100 Ω
100 Ω
100 Ω
Connect to Arduino for processing

## Slide 19: Step 1/a: Breadboarding
The electronic components are inserted in the breadboard to test the prototype circuit

## Slide 20: Step 1/b: Protoboards
Protoboards are perforated boards with copper plated holes where wire can be connected and soldered
Yasser’s first protoboard project (2010)

## Slide 21: Protoboard soldering and connection

## Slide 22: What is happening here 🤔?

## Slide 23: Correct way to hold soldering iron

## Slide 24: Very old way of making printed circuit boards
Ferric chloride etching of copper boards

## Slide 25: Use of PCB design tools such as eagle / kicad
1. Schematic design
2. Board layout
3. Fabrication

## Slide 26: Yasser’s first electronics project (14 years ago )
Before learning PCB design
After learning PCB design

## Slide 27: What’s remining now?
Build a sensor that can detect touch
3.3V
GND
50 Ω
50 Ω
50 Ω
50 Ω
50 Ω
50 Ω
100 Ω
100 Ω
100 Ω
100 Ω
Connect to Arduino for processing

## Slide 28: Arduino
https://www.youtube.com/watch?v=1ENiVwk8idM

## Slide 29: Arduino Nano 33 BLE

## Slide 30: Arduino pinout

## Slide 31: Installing and running examples on Arduino
Demo 1: Blink the LED
Demo 2: Wireless data transfer to a web app