## Slide 1: ECE 105: Introduction to Electrical Engineering
Lecture 1
Introduction to EE, and ECE 105
Yasser Khan
Rehan Kapadia

## Slide 2: What is Electrical Engineering?
Electrical Engineering is an engineering discipline concerned with the study, design, and application of equipment, devices, and systems which use electricity, electronics, and electromagnetism.

## Slide 3: Let’s look at EE at play: 3 little pigs demo by Neuralink

## Slide 4: Neuralink – the neural implant
Every step of the neural implant design and fabrication requires electrical engineering

## Slide 5: Neural interfaces – under the hood
(a) Two clinical neural interfaces: a percutaneous neural recording implant, and a deep brain stimulator. (b) Components for an implantable bidirectional (black) or closed-loop (black and gray) wireless neural interface. (c) Example neural interface electrodes. [From left to right (adapted from Utah microelectrode array [6], SENSIGHT by Medtronic [7], ultrathin polymer threads by Neuralink [8], high-density neural matrix [9], Stentrode by Synchron [10], and ultraflexible syringe-injectable mesh [11]).] LNA: low-noise amplifier; ADC: analog-to-digital converter; Tx: transmitter; ML: machine learning; DAC: digital-to-analog converter; Rx: receiver.

## Slide 6: Link v0.9
Sensors need electrical engineering, mechanical engineering, materials science, chemical engineering
Implants need electrical engineering, computer science
Surgical robots need robotics, electrical engineering, mechanical engineering, control engineering

## Slide 7: Brain recording from 1024 analog pixels
Each neural recording unit requires sensors, integrated circuits, communications, and power
Notes: 8x8 x4 x12 = 3072

## Slide 8
What is currently driving computing?

## Slide 9: How do we carry out so much computing?
We use transistors!

## Slide 10: 1956 Physics Nobel Prize

## Slide 11: What is a transistor?

## Slide 12: What is a transistor?
It acts as an on-off switch.
We want to switch it on and off as fast as possible.
We want to switch it on and off with as little power usage as possible.

## Slide 13: What do modern day integrated circuits look like?
Key points
  Total of ~150 billion transistors
  Uses 5 nm node technology
    Density of transistors is ~130-230 million transistors/mm2
    In the area of a cell , we could fit ~100k - 1 million transistors
  Multiple parts of this processor use 3-D stacked dies
    Enables computing, memory, sensing, and stimulation to be integrated together
  Performance ~8x improved over previous MI250 Accelerator
    If they upgraded the fastest supercomputer to this part, they could train the largest AI/ML systems
AMD Instinct MI300 Accelerator

## Slide 14: What do these look like?
Active devices (silicon transistors)
Wires to connect all the transistors together

## Slide 15
How did we get here?

## Slide 16: How much has computing power increased?
From 1990 to today, the worlds largest super computers have increased computing power by 100,000x
  That’s a lot!
By Our World In Data - https://ourworldindata.org/grapher/supercomputer-power-flops

## Slide 17: The First Moon Landing Was Achieved With Less Computing Power Than a Cell Phone or a Calculator
On board Apollo 11 was a computer called the Apollo Guidance Computer. It had 2,048 words of memory that could be used to store “temporary results”—data that is lost when there is no power. This type of memory is referred to as RAM (random access memory). Each word comprised 16 binary digits (bits), with a bit being a zero or a one. This means that the Apollo computer had 32,768 bits of RAM memory.
My computer has 64,000,000,000 bits of RAM memory
That is 2,000,000 times more than what was needed in Apollo 11.

## Slide 18
How do we make transistors faster?

## Slide 19
1971: The first commercial microprocessor…Intel 4004
  4-bits
  Less than 1 square inch in area
  Transistors that were 10 micrometers long
  ~750 kilohertz speed
  …but more powerful than the computers from earlier that weighed 30 tons
Let’s say that this is a scaled version of how long a transistor was in 1971
Scaling – How much have we scaled devices?

## Slide 20
1990s: The first Pentium processor
66 MHz. That’s 100 times faster than in 1970.
  Can you think of anything else that has improved by 100x in 20 years?
1971
1993
Scaling – How much have we scaled devices?

## Slide 21
2012:
  1-3 GhZ
  Multi-core
  Super-fast
  Each transistor is almost 1000 times smaller!
1971
1993
Can’t even see the size on the screen…not enough pixels
Scaling – How much have we scaled devices?

## Slide 22
What does a modern CPU cross section look like?
  Where are the transistors?
  What are we looking at?
Scaling – How much have we scaled devices?
Intel 4 cross section: to be released 2023

## Slide 23
FinFETs
  Why is it called that?
  What do you think the advantage is?
FinFET Transistors (May 2011 and After)

## Slide 24
This is a recent roadmap for Intel’s transistor scaling plans
Scaling – How much have we scaled devices?

## Slide 25
What is a Nanoribbon FET?
  Why does it give better performance?
Scaling – How much have we scaled devices?

## Slide 26: My background and research
BS, EE, 2010
MS, EE, 2012
Started PhD, 2013
Bioelectronic and Biophotonic Systems
Electrical Engineering and Materials Science
2014
2015
2016
Flexible Hybrid Electronics
PhD, EECS, 2018
Started postdoc, 2019
Wearables for precision health and psychiatry
Ventilator for COVID-19

## Slide 27: Khan Lab @ USC

## Slide 28: Khan Lab @ USC
Research Focus

## Slide 29: Soft sensor systems for precision health and psychiatry
Materials, Manufacturing, Design, Devices, and Circuits
Systems and Applications

## Slide 30: Sensors for precision health and psychiatry
Vision:
A flexible sensor patch that seamlessly measure vital signs - measurements of the body’s most basic functions
Current state:
Big machines with a lot of wired rigid sensors that limits the comfort of the patient

## Slide 31: AI-powered biosensor for detecting hand gestures
Biopotential sensing for gesture recognition

## Slide 32: Screen-printed MRI receive coils
High-throughput.
Scalable.
Fast.
Significantly less process steps compared to photolithography.
Notes: This video is a good demonstration of the potential of printed sensors. It shows printing of MRI receive coils.

## Slide 33: 3D gas mapping in the gut with AI-enabled ingestible and wearable electronics
Existing approach: Helmholtz coil for producing a region of nearly uniform magnetic field and localizing ingestible inside the coil.
Our approach: Wearable multi-layer coil for 3D field gradient, and use a bend sensor for accounting for movement.

## Slide 34: 3D gas mapping in the gut with AI-enabled ingestible and wearable electronics

## Slide 35: Kapadia Lab Research Portfolio
Back-End Materials Growth and Heterogeneous Integration
Electron Emission Devices for GHz to THz Applications
Ultra-Low Power Computing
100x

## Slide 36
$50M 12,000 Sq. ft. facility
+24,000 sq. ft. automated facility for facilities, gases, and support systems
35+ state-of-the-art cleanroom tools including e-beam and direct write tools, Si and compound semiconductor processing
Sample size from pieces to 100mm (min) and 150mm (subset – but all III-V)
Scalability:
+200 users (2024) with expansion to +500 users planned. The lab can handle 100 active users.
Space available within current facility for additional capacity and capability
Deposition
Etch
Lithography
Wet Processing
Packaging
Infrastructure
John O’Brien Nanofabrication Laboratory

## Slide 37: EE 105 Course objectives
• Understand theoretical and practical concepts in electrical engineering.
• Overview of devices, circuits, systems, and AI/ML tools.
• Design simple biosensor systems from end to end.
• Design imager systems with embedded ML.
• Design and implement electronic systems for given specifications.
Hands-on EE System design
Software
Hardware
Theory
Full-stack electronic system development

## Slide 38: Syllabus
Dynamic syllabus: https://drive.google.com/file/d/1HjTI33m4UouCzfoHWDAxYqaWjobf419k/view?usp=sharing
Prof. Yasser Khan
Emails: yasser.khan@usc.edu
Offices: MCB 270D
Atiyeh Abbasi Jalal
(Teaching Assistant)
Emails: abbasija@usc.edu
Prof. Rehan Kapadia
Emails: rkapadia@usc.edu
Offices: PHE 626
Vikas Addepalli (Course Mentor)
Emails: daddepal@usc.edu
Walter Unglaub
(Research Engineer)
Emails: unglaub@usc.edu

## Slide 39: Course structure
Lectures and discussions are sufficient for homework and final exam
Emphasis on practical learning
Homework to review major concepts
Homework | 30% (6)
Mid | 30% (October 17, Thursday )
Final | 40% (December 12, 2-4pm, cumulative)

## Slide 40: Approximate schedule
Course homepage: https://brightspace.usc.edu/d2l/home/114204
6 homework assignments
Final in finals week
Mid October 17 in class
HW 1
HW 6
Mid
Final

## Slide 41: Course content
6 homeworks are on 6 modules
  Circuits
  Devices
  Systems
  Linear algebra
  Neural network
  Communication systems
Midterm will cover circuits, devices, and biosensing systems
Final will cover everything.

## Slide 42: Custom demonstration board for EE 105
Circuits
Voltage dividers
Module 1: Circuits
Electronic devices
Diodes
Transistors
Module 2: Devices
Module 3: Systems
Electronic systems
Optical communication system
Oximeter
Module 4: TinyML
Machine vision
Arduino
Arduino Nano 33 BLE

## Slide 43: Module 1 on circuits – demo resistive touchscreen
Finds the pressed button location automatically

## Slide 44: Module 2: diodes and transistors
Characterize semiconductor diode – how do they work

## Slide 45: Module 2: diodes and transistors
Characterize semiconductor transistors – how do they work
Current through the transistors
Increasing gate voltage / opening faucet in the water analogy

## Slide 46: Module 3: optical communication
Light on
Light off

## Slide 47: Module 3: oximeter

## Slide 48: Module 3: oximeter

## Slide 49: Module 4: Machine vision
Arduino + camera + ML = identify objects / letters / faces / anything
Goal
ECE 105

## Slide 50: Next lecture: system design