## Slide 1: ECE 105: Introduction to Electrical Engineering
Lecture 11
Bio 1
Yasser Khan
Rehan Kapadia

## Slide 2: Wearables
Wearables include devices for communication, health, fitness tracking, etc.
Future generations of devices will have new capabilities (therapeutic, haptic, etc.)
New functionality depends on energy harvesting, conformal contact, etc.
Wireless communication essential for most important functions (interfacing to mobile devices, etc.)

## Slide 3: Vital signs
Vital signs include Heart Rate, Blood Pressure, Breathing Rate, Temperature
Attractive for daily monitoring
Combining all of these metrics is more useful for preventive care

## Slide 4: $380.5 billion by 2028 – wearables alone

## Slide 5: Wearable sensing
Bioelectronic – ECG, EMG, bioimpedance tomography
Flexible sensors can efficiently measure vital signs, and other biosignals from various parts of the body.
Biophotonic – Pulse oximetry
Biochemical – Sweat sensing
Types of wearable sensing

## Slide 6: Different parts of a bioelectronics system

## Slide 7: Pulse oximetry
Pulse oximetry measures blood oxygenation. Using spectrophotometry of absorptivity of blood at two distinct wavelengths, blood oxygen saturation is quantified.
Can detect hypoxemia, ie. lower than normal blood oxygenation.
ECG
Pulse Ox
Respiration
Blood
Pressure
Temperature
SO2 The saturation of oxygen in blood,
CHbO2 Concentration of oxygenated hemoglobin (HbO2),
CHb Concentration of deoxygenated hemoglobin (Hb).

## Slide 8: Oximetry - History
1864
1864, The discovery that the colored substance in blood was the carrier of oxygen was made by George Gabriel Stokes (1819-1903)
1935, Kurt Kramer (1906-1985) showed that the Lambert-Beer law applied to hemoglobin solutions and approximately to whole blood, and measured saturation by the transmission of red light through unopened arteries.
1935
1942, Glenn Allan Millikan (1906-1947) built a light-weight ear "oximeter“ during World War II to train pilots for military aviation using a mercury vapor light, yellow and purple filters, and a copper oxide photocell.
1942

## Slide 9: Oximetry - History
1864
1935
1942
Around 1964, Robert Shaw, a surgeon and inventor in San Francisco, began design and construction of a self-calibrating, eight-wavelength ear oximeter. His concept was to uniquely solve the simultaneous equations by using one more wavelength than the number of separate forms of hemoglobin needing identification.
1964
1975, Pulse oximetry was reported by Nakajima, Hirai, Takase, Kuse, Aoyagi, Kishi, and Yamaguchi of the Minoha Corporation. They used fiberoptic bundles to conduct light to and from a finger. Initially the main problem was extreme sensitivity to motion.
1975
Solid state pulse oximeter "probes" on typical locations. Ohmeda Company, Boulder, CO.

## Slide 10: Pulse oximetry basics

## Slide 11: Pulse oximeter basics

## Slide 12: The Beer-Lambert Law

## Slide 13: The Beer-Lambert Law

## Slide 14: Example 1

## Slide 15: Example 1

## Slide 16: Pulse oximeter basics

## Slide 17: Pulse oximeter basics

## Slide 18: Calculating oxygen saturation

## Slide 19: Oximeter readout circuit

## Slide 20: Oximeter readout circuit

## Slide 21: Transmission vs. reflectance oximetry
Transmission-mode pulse oximetry is limited only to tissues that can be transilluminated, such as the earlobes and the fingers.
If reflected light is used as the signal, the sensor can be used beyond the conventional sensing locations.
AC signal is the highest at the forehead for both Red and NIR channels.
Arms provide mid-range AC amplitude, while signal strength is low in the legs and chest area.
Forehead is the best location for reflectance pulse oximetry.

## Slide 22: Collect PPG signal

## Slide 23: Upload ard code

## Slide 24: Open python IDLE – open python file

## Slide 25: Open main.py

## Slide 26: Run module

## Slide 27: Type in which port – check where your Ard in connected

## Slide 28: Command – m3ppg

## Slide 29: Opens a recording window

## Slide 30: Press capture

## Slide 31: Keep your finger gently on the sensor

## Slide 32: Click save – a new file will be saved

## Slide 33: Open jupyter notebook select the new csv file – check the raw data on notebook