## Slide 1: ECE 105: Introduction to Electrical Engineering
Lecture 5
Device 1
Yasser Khan
Rehan Kapadia

## Slide 2: The First Transistor

## Slide 3: 1956 Physics Nobel Prize

## Slide 4
Invention of the Field-Effect Transistor
In 1935, a British patent was issued to Oskar Heil.
A working MOSFET was not demonstrated until 1955.

## Slide 6
Introduction to the MOSFET
Basic MOSFET structure and IV characteristics

## Slide 7
Introduction to the MOSFET
Two ways of representing a MOSFET:

## Slide 9: Complementary MOSFETs (CMOS)
When Vg = Vdd , the NFET is on and the PFET is off.
When Vg = 0, the PFET is on and the NFET is off.
NFET PFET

## Slide 10
CMOS (Complementary MOS) Inverter

## Slide 11: Qualitative discussion: n-MOSFET
VG > VT ; VDS  0
ID increases with VDS
VG > VT; VDS small, > 0
ID increases with VDS , but rate of increase decreases.
VG > VT; VDS  pinch-off
ID reaches a saturation value, ID,sat The VDS value is called VDS,sat
VG > VT; VDS > VDS,sat
ID does not increase further, saturation region.

## Slide 12: ID-VDS characteristics expected from a long channel (L << L) MOSFET (n-channel), for various values of VG

## Slide 13: ID-VDS characteristics for n-MOSFET
Saturation
region
Linear
region

## Slide 14: Quantitative ID-VDS Relationships – 1st attempt “Square Law”
;
ID will increase as VDS is increased, but when VG – VDS = VT, pinch-off occurs, and current saturates when VDS is increased further. This value of VDS is called VDS,sat. i.e., VDS,sat = VG – VT and the current when VDS= VDS,sat is called IDS,sat.
;
Here, Cox is the oxide capacitance per unit area, Cox = ox / xox

## Slide 15: P-MOSFET N-MOSFET IV Characteristics
The PMOS IV is qualitatively similar to the NMOS IV, but the current is about half as large. Why?

## Slide 16: Threshold and Subthreshold

## Slide 17: Subthreshold Current
I
d
s
(
m
A
/
m
m
)
Vgs
The leakage current that flows at Vg<Vt is called the subthreshold current. Previously we had assumed that current is zero, but in reality that’s not the case.
90nm technology. Gate length: 45nm for NMOS, 50nm for PMOS
The current at Vgs=0 and Vds=Vdd is called Ioff.
Intel, T. Ghani et al., IEDM 2003