## Slide 1: ECE 105: Introduction to Electrical Engineering
Lecture 10
Device 2
Yasser Khan
Rehan Kapadia

## Slide 2: What is a diode
A diode is a device that exhibits ‘rectifying’ behavior
Can be made from a physical junction between an n-type semiconductor and a p-type semiconductor
Can also be made from a physical junction between a metal and semiconductor (not discussed here)

## Slide 3: Forward biasing a diode

## Slide 4: Reverse biasing a diode

## Slide 5: Diode characterization

## Slide 6: Water analogy

## Slide 7: Diode Current Equation
This equation partially describes the behavior of a non-ideal diode

## Slide 8: Diode Current Equation

## Slide 9: Diode Current Equation

## Slide 10: The First Transistor
December 16, 1947: John Bardeen and Walter Brattain successfully demonstrated the first working transistor at Bell Labs.
It was a point-contact transistor made of a small slab of germanium with two closely spaced gold contacts.
When input current was applied to one contact, it modulated the conductivity of the germanium, amplifying the signal seen at the other contact.
Key outcome: It could amplify electrical signals like a vacuum tube, but in a device only a few millimeters wide.
At Bell Telephone Laboratories, research was focused on finding a solid-state amplifier for telephone signal processing.
The three key scientists were:
John Bardeen (theorist)
Walter Brattain (experimentalist)
William Shockley (team leader, physicist)

## Slide 11: Transistor amplification

## Slide 12: 1956 Physics Nobel Prize

## Slide 13
Invention of the Field-Effect Transistor
In 1935, a British patent was issued to Oskar Heil.
A working MOSFET was not demonstrated until 1955.

## Slide 17
Introduction to the MOSFET
Basic MOSFET structure and IV characteristics

## Slide 18
Introduction to the MOSFET
Two ways of representing a MOSFET:

## Slide 20: Complementary MOSFETs (CMOS)
When Vg = Vdd , the NFET is on and the PFET is off.
When Vg = 0, the PFET is on and the NFET is off.
NFET PFET

## Slide 21: ID-VDS characteristics expected from a long channel (L << L) MOSFET (n-channel), for various values of VG

## Slide 22: MOSFET current equations

## Slide 23: MOSFET current equations

## Slide 24: MOSFET current equations

## Slide 25
CMOS (Complementary MOS) Inverter

## Slide 26
CMOS (Complementary MOS) Inverter

## Slide 27
CMOS (Complementary MOS) Inverter

## Slide 28
CMOS (Complementary MOS) Inverter

## Slide 29: Qualitative discussion: n-MOSFET
VG > VT ; VDS  0
ID increases with VDS
VG > VT; VDS small, > 0
ID increases with VDS , but rate of increase decreases.
VG > VT; VDS  pinch-off
ID reaches a saturation value, ID,sat The VDS value is called VDS,sat
VG > VT; VDS > VDS,sat
ID does not increase further, saturation region.

## Slide 30: Quantitative ID-VDS Relationships – 1st attempt “Square Law”
;
ID will increase as VDS is increased, but when VG – VDS = VT, pinch-off occurs, and current saturates when VDS is increased further. This value of VDS is called VDS,sat. i.e., VDS,sat = VG – VT and the current when VDS= VDS,sat is called IDS,sat.
;
Here, Cox is the oxide capacitance per unit area, Cox = ox / xox

## Slide 31: ID-VDS characteristics for n-MOSFET
Saturation
region
Linear
region

## Slide 32: P-MOSFET N-MOSFET IV Characteristics
The PMOS IV is qualitatively similar to the NMOS IV, but the current is about half as large. Why?

## Slide 33: Threshold and Subthreshold

## Slide 34: Subthreshold Current
I
d
s
(
m
A
/
m
m
)
Vgs
The leakage current that flows at Vg<Vt is called the subthreshold current. Previously we had assumed that current is zero, but in reality that’s not the case.
90nm technology. Gate length: 45nm for NMOS, 50nm for PMOS
The current at Vgs=0 and Vds=Vdd is called Ioff.
Intel, T. Ghani et al., IEDM 2003