## Slide 1: ECE 105: Introduction to Electrical Engineering
Lecture 9
Device 1
Yasser Khan
Rehan Kapadia

## Slide 2: Semiconductor devices

## Slide 3: Chip War
https://www.youtube.com/watch?v=foYWzdvajvo

## Slide 4: How can we create tunable resistors?
R = rL/A
We have three options, change length, change area, or change resistivity
Semiconductors allow us to electromagnetically and chemically control resistivity

## Slide 5: How do semiconductors allow us to tune the resistivity?
By allowing us to tune the density of charge carriers!
In metals, the density of charge carriers is ~ 1022 -1023/cm3
In insulators, the charge density is ~10-57/cm3
In semiconductors, the charge density can be controlled from ~1010/cm3 – 1020/cm3

## Slide 6: What can we do with an element that has tunable or non-linear resistance?
Create a switch
  Digital logic
Amplify a signal
  Analog circuits
Rectify an AC voltage
  Power circuits
Sensing, power generation, light, etc

## Slide 7: Why does changing the carrier density change the resistivity?
Let’s revisit R = rL/A
If I take a material and magically stuff additional mobile electrons into it, then the resistivity would decrease.
If I remove additional mobile electrons from it, then the resistivity would increase.
So if I had a material which allows me to change the mobile charge density, then I can tune the resistivity of that material

## Slide 8: What’s after resistors, capacitors, and inductors
Each device and circuit allows us to carry out specific functionalities

## Slide 9: What are semiconductors
Elements: Si, Ge, C
Binary: GaAs, SiC, CdSe, etc.
Ternary+: AlGaAs, InGaAs, etc.

## Slide 10: Silicon – the workhorse of electronics

## Slide 11: Silicon Crystal Structure
Unit cell of silicon crystal is cubic.
Each Si atom has 4 nearest neighbors.
Electrons and Holes in Semiconductors
Å

## Slide 12: Bond Model of Electrons and Holes (Intrinsic Si)
·
Silicon crystal in
a two-dimensional
representation.
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
·
When an electron breaks loose and becomes a
conduction
electron
, a
hole
is also created.

## Slide 13: Dopants in Silicon
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
As
B
·
As (Arsenic), a Group V element, introduces conduction electrons and creates
N-type silicon,
·
B (Boron), a Group III element, introduces holes and creates P-type silicon,
and is called an acceptor.
·
Donors and acceptors are known as dopants.
and is called a donor.
N-type Si
P-type Si

## Slide 14: GaAs, III-V Compound Semiconductors, and Their Dopants
As
As
Ga
Ga
·
GaAs has the same crystal structure as Si.
·
GaAs, GaP, GaN are III-V compound semiconductors, important for
optoelectronics.
·
Which group of elements are candidates for donors? acceptors?
Ga
As
As
Ga
Ga

## Slide 15: Energy Band Diagram
Conduction band
E
c
E
v
E
g
Band gap
Valence band
·
Energy band diagram shows the bottom edge of conduction band, Ec , and top edge of valence band, Ev .
·
Ec and Ev are separated by the band gap energy, Eg .

## Slide 16: Measuring the Band Gap Energy by Light Absorption
photons
photon energy: h
v
> E
g
E
c
E
v
E
g
electron
hole
Bandgap energies of selected semiconductors
Eg can be determined from the minimum energy (hn) of photons that are absorbed by the semiconductor.
Material
PbTe
Ge
Si
GaAs
GaP
Diamond
E
g
(eV)
0.31
0.67
1.12
1.42
2.25
6.0

## Slide 17: Semiconductors, Insulators, and Conductors
·
Totally filled bands and totally empty bands do not allow
·
Metal conduction band is half-filled.
E
c
E
v
E
g
=
1.1 eV
E
c
E
g
=
9 eV
empty
Si (Semiconductor)
SiO
2
(Insulator)
Conductor
E
c
filled
Top of
conduction band
E
v
current flow. (Just as there is no motion of liquid in a totally filled or totally empty bottle.)
.
·
Semiconductors have lower E
g
's than insulators and can be
doped.

## Slide 18: Resistance calculation and changing by doping

## Slide 19: Resistance calculation and changing by doping

## Slide 20: Resistance calculation and changing by doping

## Slide 21: Resistance calculation and changing by doping
N-type
P-type
 = 1/
DOPANT DENSITY cm-3
RESISTIVITY (cm)
(a) What is the resistivity () of silicon doped with 1017cm-3 of arsenic?
Solution:
(a) Using the N-type curve in the previous figure, we find that  = 0.084 -cm.
(b) What is the resistance (R) of a piece of this silicon material 1m long and 0.1 m2 in cross-sectional area?
(b) R = L/A = 0.084 -cm  1 m / 0.1 m2
= 0.084 -cm  10-4 cm/ 10-10 cm2
= 8.4  10-4 

## Slide 22: What is a diode
A diode is a device that exhibits ‘rectifying’ behavior
Can be made from a physical junction between an n-type semiconductor and a p-type semiconductor
Can also be made from a physical junction between a metal and semiconductor (not discussed here)

## Slide 23: Forward biasing a diode

## Slide 24: Reverse biasing a diode

## Slide 25: Diode characterization

## Slide 26: Water analogy

## Slide 27: Diode Current Equation
This equation partially describes the behavior of a non-ideal diode

## Slide 28: Diode Current Equation

## Slide 29: Diode Current Equation