## Slide 1: EE-105 Arduino Installation
9/2/2025

## Slide 2
What is Arduino?
Microcontroller Development Board
Open-source hardware + software.
Simple programming with Arduino IDE.
Used for rapid prototyping.
Why use Arduino?
Low cost and widely available.
Large community and libraries.
Easy to connect sensors/actuators.
Good entry point into embedded systems.
Different types of Arduino Boards

## Slide 3
Arduino Nano 33 BLE

## Slide 4
Installing the Arduino IDE
Connect the USB cable to Arduino
Download the latest release of the Arduino IDE here
https://support.arduino.cc/hc/en-us/articles/360019833020-Download-and-install-Arduino-IDE

## Slide 5
1
2
3

## Slide 6
2.Ensure that the Mbed OS Nano Boards package is installed
Tools -> Board: -> Boards Manager... -> Install "Arduino Mbed OS Nano Boards"
1. Identify the COM port that Arduino is connected

## Slide 7
void setup() {
// initialize digital pin LED_BUILTIN as an output.
pinMode(LED_BUILTIN, OUTPUT);
}
// the loop function runs over and over again forever
void loop() {
digitalWrite(LED_BUILTIN, HIGH); // turn the LED on (HIGH is the voltage level)
delay(1000); // wait for a second
digitalWrite(LED_BUILTIN, LOW); // turn the LED off by making the voltage LOW
delay(1000); // wait for a second
}

## Slide 8
// Pin number for the built-in LED
const int ledPin = 13;
void setup() {
// initialize digital pin 13 as an output.
pinMode(ledPin, OUTPUT);
}
void loop() {
digitalWrite(ledPin, HIGH); // turn the LED on (HIGH is the voltage level)
delay(1000); // wait for a second
digitalWrite(ledPin, LOW); // turn the LED off by making the voltage LOW
delay(1000); // wait for a second
}
Another way of coding

## Slide 9
Streaming Sensor Data to a Web App
Let’s start using Arduino Cloud https://cloud.arduino.cc/?gad_source=1&gbraid=0AAAAACbEa84ofzTu6ZqKTNrvfC00iYeOK&gclid=CjwKCAjwlbu2BhA3EiwA3yXyuyRs52Pa6IMOnlhxourjC6ZlovP8tXgo2qfPTzjIE3rKl_pymK4kmxoCDSMQAvD_BwE
2. You need to install Arduino Cloud Agent: You need Arduino cloud agent to be able to detect or interact with your Arduino board, because web browsers don’t have direct access to your computer’s hardware.
https://support.arduino.cc/hc/en-us/articles/360014869820-Install-the-Arduino-Create-Agent

## Slide 10
Sketches  Create
Copy the Blink code into Arduino cloud and upload to verify that the cloud IDE is working.

## Slide 11
Webapp link: https://arduino.github.io/ArduinoAI/BLESense-test-dashboard/
Upload this code to Arduino nano 33 ble to be able to stream the sensor data to a webapp
https://app.arduino.cc/sketches/71cdba81-1380-4aee-9cb1-14cde2da7607?view-mode=preview
How can we monitor the streamed data?

## Slide 12
1.After uploading the code, click on the green button
2. Now your Arduino BLE will pair with the web app
3. The sensor data is streaming to the web app

## Slide 13
Testing pressure sensor
https://app.arduino.cc/sketches/4573b54c-d240-41b0-94a4-4ac0dca97e66?view-mode=preview
Using the Serial Monitor
Your serial monitor output should look like this

## Slide 14
APDS9960: Detects ambient light, color, proximity, and gestures.
LPS22HB: Measures atmospheric pressure
LSM9DS1: Tracks acceleration, rotation, and magnetic field orientation.
PDM Microphone: Captures and analyzes sound signals.
RGB LED: Provides visual feedback with controllable colors.
The Arduino Nano 33 BLE is equipped with several built-in sensors, making it a powerful tool for various applications without needing additional hardware.

## Slide 15
Color Detection: The Colorimeter function in the web app is designed to detect and analyze the color of objects in the sensor's view. The APDS9960 sensor can measure the intensity of red, green, and blue light (RGB values) that is reflected from an object or present in the environment.
Proximity Sensor: This sensor can detect objects within a certain distance, ranging from a few centimeters up to about 10 centimeters. It is commonly used in gesture control applications, where you can interact with devices without physical contact.
Gesture Detection: The APDS9960 can recognize simple gestures like up, down, left, and right swipes. This feature enables touchless interaction with devices, such as controlling media playback or navigating menus with hand gestures.

## Slide 16
Accelerometer: This sensor measures acceleration forces along the X, Y, and Z axes. It is used to detect movement, orientation, and vibration. Applications include motion tracking, tilt sensing, and detecting free fall in devices like smartphones and wearables.
Gyroscope: The gyroscope measures angular velocity (rotation) around the X, Y, and Z axes. It is used to detect and control the orientation of an object in 3D space. Common applications include stabilization in drones, gesture recognition, and gaming controllers.
Microphone: The PDM microphone captures audio signals by converting sound waves into electrical signals. The microphone’s data is processed using an FFT (Fast Fourier Transform) to analyze the frequency components of the sound.
Spectrogram is a visual representation of the spectrum of frequencies in a signal as it varies with time. In this case, the code is generating a spectrogram from audio data captured by a microphone, likely using the PDM (Pulse Density Modulation) microphone on the Arduino Nano 33 BLE Sense

## Slide 17
Classwork 1
Write a function in Arduino that can be used to change the frequency of LED blinking.
Hint: This is how to define a function in the C programming language.